## Slide 1: Extreme Terrain Quadruped (ET-Quad) For Traversing Rocks, Regolith, and Rough Terrain
Florida A&M University and Florida State University
FAMU-FSU College of Engineering
Presenters: Derek Vasquez, David Jay, and Michael Dina
Team members: Hamza Asif, Max Austin, Dominic Bellocchio, Jonathan Boylan, Andrew Burkhardt, Ashley Chase, Justin Cheesborough, Alejandro Chong-Garcia, Jayson Dickinson, Michael Dina, William Hochstedler, David Jay, Geraina Johnson, Benjamin Labiner, Francisco Lopez, Joseph Lupton, Gissel Reynoso, Cameron Ryals, Carlos Sanchez-Sarmiento, Dane Seal, Zaid Shah, Brian Van Stratum, Derek Vasquez, Jason White
Faculty advisors: Jonathan Clark, Christian Hubicki, Camilo Ordonez, Shane McConomy, Juan Ordonez

## Slide 2
ET-Quad Abstract
2 new planning algorithms for multimodal lunar locomotion
First legged robot capable of walking, climbing vertical surfaces, and traversing resistive media (water, regolith)
Novel leg design integrates capabilities and lessons from biology and previous single mode robots

## Slide 3
Notes: Avoid causation language

## Slide 5
M. Austin et al., "Optimizing Dynamic Legged Locomotion in Mixed, Resistive Media," 2022 IEEE/ASME International Conference on Advanced Intelligent Mechatronics (AIM), 2022, pp. 1482-1488, doi: 10.1109/AIM52237.2022.9863276.

## Slide 6: Modal Locomotion Decomposition
Terrestrial
Scansorial
Resistive Media
Modal Demux

## Slide 7
Legged Multimodal Robots
Aquatic
Scansorial
Terrestrial
?

## Slide 8
Objective: Build a single robotic platform with animal-like capabilities to address each of these locomotion challenges on the moon

## Slide 9
Reduced Order Modeling Methodology
Biological Synthesis
Dimensional Collapse
Robot Design
Modeling Methods of Dynamic Legged Locomotion

## Slide 10
Aquatic
Scansorial
Terrestrial
Modeling Methods of Dynamic Legged Locomotion
Full-Goldman Model
FF-SLIP
LPS
M. Austin, A. Chase, B. Van Stratum, and J. E. Clark, “Aquaclimber: a limbed swimming and climbing robot based on reduced order models,” Bioinspiration & Biomimetics, 2022.
M. Austin et al., "Optimizing Dynamic Legged Locomotion in Mixed, Resistive Media," 2022 IEEE/ASME International Conference on Advanced Intelligent Mechatronics (AIM), 2022, pp. 1482-1488

## Slide 11: Dyna-Kinematic Leg Design
Optimized Leg
Optimization
Actuator Model
L1
L2
L2
L1
L1
L2
L3
L4
L5
L6
Designer Selected Leg Mophologies
Designer Selected Locomotion
Target Dynamics
Kinematic Mapping
Jacobian
Mappings
Constraints
Feasible Subset
Mapping between the behavior(s) and your achievable design space
Approximation of the robot engaging in the behavior(s)
Possible causes of failure & requisite design features
Task regime: What do you want the robot to do?
Selecting a locally optimal morphology to implement
Austin, M., Brown, J., Nicholson, J., and Clark, J. (November 8, 2022). "Dyno-Kinematic Leg Design for High Energy Robotic Locomotion." ASME. J. Mechanisms Robotics. June 2023; 15(3): 031001.
66 mm
180 mm
Geometric symmetry
Concentric drive shafts
6:1 gear reduction on one link

## Slide 12
Scansorial
Terrestrial
Full-Goldman Model
FF-SLIP
LPS
Aquatic
Different compliance requirements
Foot Design
1x stiffness
2x stiffness
Design Requirements
Anisotropic compliance
Attachment capability for climbing
Sufficient traction for walking
Directional drag for swimming
Lemur
RHeX
Aqua

## Slide 13
Flap provides directional drag
Claws grab substrate
Kurfing allows anisotropic compliance (tuned for walking and climbing)
Foot Design
High friction ground contact point

## Slide 14
Embedded hook increases reliability
Increased ground contact for traction
More resilient material
AR500 abrasion resistant steel
10% mass reduction
Improved Foot Design
Toes extend independently to grab small asperities
Fin increases drag 2.5x

## Slide 15
System Overview
Four hip assemblies with 2x brushless DC motors with Kv of 330 and 1.7 Nm peak torque. Gearing provides 6:1 reduction on one link and coaxial output shafts.
Sensor suite: Lidar and depth camera
2x 4-cell lithium polymer batteries with 2800 A h each.
4 Raspberry Pi Model 4b’s provide control at ~230 Hz to 8 motors. Also capable of mapping at ~7 Hz, local planning at 45 Hz, and global planning at ~1 Hz.
Power management board distributes up to 80 A to motors and computation. Measures power consumption.
Body is waterproof to ISO 22810 standards.
Skids protext robot underbelly when climbing.
Full system mass: 7.85 kg

## Slide 16
Sensors and Autonomy
2D Hokuyu UTM-30LX LiDAR
Realsense d435i stereo depth camera
4x Raspberry Pi Model 4b for mapping, planning, control, and communications
6-axis inertial measurement unit (IMU)/gyroscope and temperature sensor
0.85 kg total
Sensors
Onboard Network
(roscore)
Rpi 1
(Path Planning)
LiDAR
RealSense
Depth Camera
IMU
Rpi 3
(Motor Control)
Rpi 2
(Mapping)
Hip Module 1
Hip Module 2
Hip Module 3
Hip Module 4
Base Station
Computer
Vicon MoCap
System
Motors
map
Desired body velocity
Goal coordinates
Localization
Low level control
KEY:
Network ROS communication
Serial
CAN

## Slide 17
Sensors and Autonomy - Demonstration
Obstacles
Climbable slope
Goal Point
Goal Point
Climbable slope
Obstacles
Planned path
Camera view
Third person view

## Slide 18
Aquatic
Scansorial
Terrestrial
?
ET-Quad in Robotics State-of-the-art

## Slide 20
Sensors and Autonomy

## Slide 21
Ongoing Integrations: Planning for Multimodality
When should the robot walk, climb, or swim?
Climbable slope
Obstacle
Colors represent gaits
Run
Walk
Climb
Not traversible
Map with path to goal

## Slide 22
Ongoing Implementation: Planning for Lunar Thermal Challenges
How can we account for temperature variations on the moon?
Time varying temperature gradient
Plan path through sunny regions
Energy efficient paths through moderate temperatures to the goal
Hot regions
Cold regions
Sampling based model predictive optimization (SBMPO)

## Slide 23: Review
First legged robot capable of walking, vertical climbing, and swimming
Multimodal legs and feet allow trimodal locomotion without hardware changes
Thermally informed planning allows energy efficient locomotion in changing lunar illumination
3D mapping for multimodal locomotion planning

## Slide 24
Thank you!
Michael Dina
mdina@fsu.edu
Shayne McConomy
smcconomy@eng.famu.fsu.edu
Jonathan Clark
clarkj@eng.famu.fsu.edu
David Jay
djay@fsu.edu
Derek Vasquez
davasquez@fsu.edu